## Slide 1
YUVA YODHA 2026 · CHALLENGE 01: SUSTAINABLE AGRICULTURE
AgroStruxure™
Solar-synchronised agri-energy microgrid and precision irrigation for PM-KUSUM pumps
“One solar pump can become a rural energy node.”
A retrofit kit that caps irrigation at what the crop needs, so free daytime solar cannot over-pump the aquifer, then runs a shared farm-gate pre-cooler from the idle surplus.
41.2%
less groundwater
7,000 m³/ha/yr
63%
of PV output idle
after right-sizing water
1.31 t
tomatoes saved
per ha per year
2.0 yr
capital payback
₹50,212 net per farm
Sanskar Tiwari (Firmware, lead) · Shambhavi Patil (Geospatial) · Kanishka Salgude (Power / VFD) · Chaitanya Ranade (Agronomy / Product)
ONE PUMP · TWO LOADS · ONE CONTROLLER
4.8 kWp PV array
6,559 kWh per year
AgroStruxure edge controller
FAO-56 budget · field-capacity cutoff · TeSys changeover
Right-sized drip
Altivar ATV320 pump
2,422 kWh/yr
Shared pre-cooler
4-farm cluster
1,062 kWh/yr
−41.2% groundwater
−52% farm-gate loss
Altivar Solar ATV320 · TeSys D · Modbus RTU · EcoStruxure-aligned
Model: research/08_IMPACT/impact_model.py (1 ha tomato, Nashik, 4.8 kWp PM-KUSUM Component B pump). 63% idle PV = after irrigation is right-sized (37% idle today).
Notes: HOOK (20 s). One solar pump becomes a rural energy node: AgroStruxure is a retrofit kit for PM-KUSUM Component B pumps. It does two things: (1) caps irrigation at the crop's FAO-56 entitlement, which protects the aquifer from the solar rebound effect; (2) uses the idle midday solar to run a shared farm-gate pre-cooler for tomatoes. Headline numbers, all per hectare of tomato in Nashik: 41.2% less groundwater (7,000 m3/yr), 4,137 kWh/yr of PV output (63%) with no pumping use once water is right-sized, 1.31 t of tomatoes saved, 2.0-year payback on the farmer's share of a 4-farm pre-cooler. 63% idle is AFTER right-sizing; today with flood irrigation 37% (2,442 kWh) is idle. Team roster to be confirmed before submission.

## Slide 2
PROBLEM · THE SOLAR REBOUND EFFECT
Free Solar Power Accelerates Groundwater Collapse
Under PM-KUSUM Component B, daytime pumping costs nothing, so nothing limits the water drawn, and the sun goes unused.
Annual energy, one 4.8 kWp pump
1 ha tomato, kWh per year
Chart: 
| Solar generation | Pumping today (flood) | Pumping right-sized
Series | 6559 | 4118 | 2422
Today: 2,442 kWh idle (37%).
Right-sized: 4,137 kWh idle (63%), because the pump now needs 1,696 kWh less.
01
Free power, unlimited pumping
Flood irrigation applies 17,000 m³/ha/yr against a 10,000 m³ crop entitlement. Zero marginal cost removes any reason to stop.
16–39%
more water pumped after solarisation (Rajasthan study, IWMI)
02
Solar capacity stranded
Once the water is right-sized, most of the array's output has no pumping use: a stranded asset at midday.
63%
of PV output idle after right-sizing water
03
Harvest rots where the power is
No cold chain at the farm gate: tomatoes are lost at farm stage (11.62% including market handling).
8.37%
farm-stage tomato loss (NABCONS 2022, MoFPI)
Sources: CGWB National Compilation 2023 (736 of 6,553 assessment units over-exploited) · NABCONS 2022 for MoFPI · IWMI (Shah et al.) · MNRE PM-KUSUM progress (≈10.06 lakh Component B pumps installed by 31 Jan 2026). Model: research/08_IMPACT/impact_model.py (1 ha tomato, Nashik, 4.8 kWp PM-KUSUM Component B pump).
AgroStruxure™ · 02 / 10
Notes: PROBLEM (45 s). Three linked failures. (1) Rebound: PM-KUSUM makes daytime power free, so farmers pump until fields flood. Baseline flood use is 850 mm x 2 seasons = 17,000 m3/ha/yr versus a 10,000 m3 FAO-56 entitlement. IWMI-cited research reports 16-39% more extraction after solarisation in Rajasthan (verify exact citation before quoting). (2) Stranded solar: PV generates 6,559 kWh/yr; flood pumping uses 4,118 kWh, leaving 2,442 kWh idle (37%). Right-size the water and pumping falls to 2,422 kWh, so 4,137 kWh (63%) is idle. (3) Post-harvest: NABCONS 2022 farm-stage tomato loss is 8.37% (11.62% including market). Context: CGWB 2023 lists 736 of 6,553 assessment units as over-exploited; about 10.06 lakh Component B pumps were installed by 31 Jan 2026 (MNRE, as reported; 13.3 lakh sanctioned).

## Slide 3
ARCHITECTURE · ECOSTRUXURE-ALIGNED, EDGE-FIRST
One Retrofit Kit, Three Flows: Data, Energy, Money
Sensing, switching and settlement in one design. The controller works offline; the cloud only advises.
DATA
sense → advise
ENERGY
DC bus → loads
MONEY
subsidy → payback
Field sensors
FDR probes at 10 and 30 cm · flow meter · SHT31 · pyranometer
Edge controller
ESP32-S3 · FAO-56 budget · field-capacity cutoff · commands the changeover
4G gateway → FastAPI
Validated JSON (Pydantic) · read-only AI copilot
WhatsApp voice advice
Marathi / Hindi · no app, no dashboard
4.8 kWp PV array
6,559 kWh/yr · 350–600 V DC bus
TeSys D changeover
2× LC1D09BD interlocked · 5 s dead-band at 0 A
Load A · ATV320 pump
2,422 kWh/yr · 08:30–11:30
Load B · cluster cooler
1,062 kWh/yr · 11:30–15:30
Idle headroom
3,075 kWh/yr (47% of PV). Not claimed as a benefit
35% MIDH / AIF subsidy
₹108,150 off a ₹309,000 net system cost
Farmer capex
₹50,212 per farm (4-farm cluster) + ₹2,400/yr opex
Annual farmer gain
₹15,732 spoilage saved + ₹12,000 timing = ₹27,732
Capital payback
2.0 years (3.0 without subsidy)
Standards: IEC 60947-4-1 (TeSys D) · Altivar ATV320 Modbus: Reg 8501 command word, 8502 speed reference · Schneider EcoStruxure 3-tier pattern (connected products → edge control → apps & analytics).
AgroStruxure™ · 03 / 10
Notes: ARCHITECTURE (60 s). Read the three lanes top to bottom. DATA: dual-depth FDR probes, pulse flow meter and SHT31/pyranometer feed an ESP32-S3 running a deterministic FAO-56 water budget. Control never depends on the cloud; 4G only ships validated JSON to a FastAPI service that drives the WhatsApp voice advisory. ENERGY: the 4.8 kWp array feeds a 350-600 V DC bus. A mechanically interlocked pair of TeSys D contactors transfers power between Load A (Altivar ATV320 pump, 2,422 kWh/yr) and Load B (3.8 kW DC compressor, 1,062 kWh/yr for a 4-farm cluster) with a 5 s zero-current dead-band. About 3,075 kWh/yr (47% of PV) stays as headroom and is not claimed. MONEY: 35% MIDH/AIF capital subsidy, farmer pays Rs 50,212 per farm as a share of a 4-farm pre-cooler, gains Rs 27,732/yr (Rs 15,732 spoilage + Rs 12,000 price timing) against Rs 2,400/yr opex: payback 2.0 years (3.0 without subsidy). Official deliverable 2 asks for data/energy/money flows; this slide is that diagram.

## Slide 4
HYDROLOGY · CLOSED-LOOP WATER BUDGETING
41.2% Less Groundwater, Full Crop Requirement Met
A dual-Kc FAO-56 budget sets the entitlement; dual-depth FDR probes stop the pump at field capacity.
Dual-depth soil moisture profile
0–10 cm · surface probe
Evaporative zone, typically 18–32% VWC. Tracks diurnal loss.
10–40 cm · root-zone probe
Irrigation stops at field capacity (45% VWC), so there is no root-zone hypoxia.
40 cm + · deep percolation
Pulsed drip leaves nothing to leach below the root zone.
Cutoffs are calibrated per soil type.
Water applied, m³ per hectare per year
Chart: 
| Flood | Conventional drip | AgroStruxure
Series | 17000 | 12000 | 10000
7,000 m³
conserved per ha per year
5,000 m³ from drip hardware
2,000 m³ from the entitlement cap, locked against rebound
Per hectare per year | Flood | AgroStruxure | Change
Water applied | 17,000 m³ | 10,000 m³ | −7,000 m³
Pumping electricity | 4,118 kWh | 2,422 kWh | −1,696 kWh
Assumes drip is already installed (existing or subsidised). Drip hardware is not in the capex.
FAO Irrigation & Drainage Paper 56 (Allen et al.) · Flood baseline 850 mm × 2 seasons; entitlement ETc 450 mm ÷ 0.90 drip efficiency → 500 mm; 0.242 kWh/m³ at 40 m head. Model: research/08_IMPACT/impact_model.py (1 ha tomato, Nashik, 4.8 kWp PM-KUSUM Component B pump).
AgroStruxure™ · 04 / 10
Notes: WATER (60 s). Baseline is unmetered flood irrigation at 850 mm per season, two seasons: 17,000 m3/ha/yr. AgroStruxure schedules to the FAO-56 entitlement: ETc 450 mm divided by 0.90 drip efficiency = 500 mm per season, 10,000 m3/yr. Saving 7,000 m3 = 41.2%. Honest attribution: conventional drip at 600 mm would already save 5,000 m3 (29.4 points); the AgroStruxure entitlement cap adds 2,000 m3 (11.8 points) and is what locks the saving against the rebound effect. The farmer needs drip in place for this: it is an assumption, not in the capex. Pumping energy at 0.242 kWh/m3 (40 m TDH, 45% wire-to-water) falls from 4,118 to 2,422 kWh. Yield is protected because the entitlement meets full crop ET; no yield uplift is claimed.

## Slide 5
POWER ENGINEERING · UPSTREAM DC BUS ROUTING
Cooling a 4-Farm Cluster Uses 26% of One Farm's Idle Solar
Power is switched upstream on the DC bus at zero current, so no inductive spike reaches the drive.
Where the host farm's 6,559 kWh/yr goes (kWh)
Chart: 
| PV output
Pumping 37% | 2422
Cluster cold chain 16% | 1062
Headroom 47% | 3075
1,062 kWh = 26% of the 4,137 kWh surplus. 60 batches a year (4 farms × 15) at 17.7 kWh each. Headroom is reported, not claimed.
Single-line diagram
PV array
350–600 V DC
TeSys D
interlocked
ATV320 pump
3.8 kW cooler
Five-step zero-current transfer
1
Saturation or quota reached
30 cm probe hits 45% field capacity, or the daily entitlement is used.
T = 0 s
2
Controlled VFD ramp-down
Modbus Reg 8502 takes the ATV320 to 0 Hz over 8 s.
0 → 8 s
3
Zero-flow valve closure
Latching solenoid shuts at zero velocity: no water hammer.
T = 8 s
4
5 s DC dead-band
Bus capacitors discharge and DC current reaches 0 A.
8 → 13 s
5
TeSys D transfer
Interlocked contactor energises the 3.8 kW compressor.
T = 13.2 s
Break-before-make interlock per IEC 60947-4-1 · Type-2 DC SPD rated 1,000 V DC · LC1D09BD dual interlocked pair, 150 ms break, 5 s dwell. Model: research/08_IMPACT/impact_model.py (1 ha tomato, Nashik, 4.8 kWp PM-KUSUM Component B pump).
AgroStruxure™ · 05 / 10
Notes: POWER (60 s). Honest energy partition for the host farm's 4.8 kWp array: 6,559 kWh/yr. Pumping uses 2,422 kWh (37%). The shared 2 MT pre-cooler serves a 4-farm cluster: 4 farms x 15 batches = 60 batches/yr, 17.7 kWh each (13.7 kWh pull-down at COP 3.0 + 4.0 kWh hold) = 1,062 kWh, i.e. 26% of the host farm's 4,137 kWh surplus and 16% of its PV output. The other three farms' arrays are not used. 3,075 kWh (47%) stays as headroom, shown for transparency and NOT counted in any benefit. Note the correction vs earlier drafts: cooling energy follows tonnes cooled (120 t/yr for the cluster = 33% of the room's 360 t/yr capacity), not days of operation. Safety: transfer happens only at 0 A after an 8 s ramp-down, closed solenoid and 5 s dead-band; the TeSys pair is mechanically and electrically interlocked.

## Slide 6
THERMAL ENGINEERING · DECENTRALISED COLD CHAIN
Halving Farm-Gate Tomato Spoilage: 8.37% to 4.00%
A shared 2 MT pre-cooler pulls harvest-hot tomatoes from 32 °C to a safe 12 °C within four hours.
Illustrative image
1.31 t
tomatoes saved per ha per year (2.51 t → 1.20 t)
₹15,732
spoilage saved per year at ₹12/kg
₹12,000
price timing: hold crates for the evening mandi (+₹1–2/kg on 8 t)
Farm-stage loss, % of harvest
Chart: 
| Today | With pre-cooling
Series | 8.37 | 4
Thermal physics
41 kWh of heat removed per 2 MT batch (32 → 12 °C).
13.7 kWh of electricity at COP 3.0: 3.43 kW for 4 h, within the 4.8 kWp array.
12 °C setpoint avoids chilling injury below 10 °C. Phase-change plates hold overnight.
Net farmer gain ₹25,332 per year = ₹15,732 + ₹12,000 − ₹2,400 opex
Embodied emissions avoided: 0.39 t CO₂e per ha per year
Sources: NABCONS 2022 for MoFPI (tomato farm-stage loss 8.37%, total 11.62%) · 12 °C chilling threshold per ICAR-CIPHET guidance · 30 t/ha/yr yield, ₹12/kg farm-gate price are model assumptions. Model: research/08_IMPACT/impact_model.py (1 ha tomato, Nashik, 4.8 kWp PM-KUSUM Component B pump).
AgroStruxure™ · 06 / 10
Notes: COLD CHAIN (45 s). NABCONS 2022 reports 8.37% farm-stage loss for tomato (11.62% in total). Rapid pull-down to 12 C is assumed to cut farm-stage loss to 4.00%, not zero. On a 30 t/ha/yr yield that preserves 1.31 t, worth Rs 15,732 at Rs 12/kg. Price timing (holding crates for the evening mandi, +Rs 1-2/kg on 8 t) adds Rs 12,000 and is price-volatile (medium confidence). Opex Rs 2,400/yr. Net Rs 25,332/yr. Thermal: 2,000 kg x 3.7 kJ/kg.K x 20 K = 41.1 kWh thermal, 13.7 kWh electric at COP 3.0, 3.43 kW over a 4 h window. Carbon: only the embodied emissions of tomatoes that are NOT wasted are counted: 1.31 t x 0.30 kg CO2e/kg = 0.39 t CO2e/ha/yr. Solar cooling is not credited against diesel because smallholders have no cooling today. The 4.00% post-cooling loss is a design target to be measured in the pilot.

## Slide 7
COGNITIVE TRUST · DETERMINISTIC VERNACULAR AI
Vernacular Advice Grounded in Hardware Truth
Spoken Marathi and Hindi advisories on WhatsApp. The AI can read telemetry; it can never switch a contactor.
Four-stage trust pipeline
1
Edge telemetry
MCU logs FDR moisture, flow and VFD status over Modbus RTU.
2
Schema validation
Pydantic checks every JSON record; bad data blocks the model.
3
Read-only RAG prompt
Copilot sees telemetry and agronomy templates, with no tool access.
4
Voice synthesis
Marathi / Hindi audio delivered as a WhatsApp voice note.
{"vwc_30cm": 0.448, "status": "FC_CUTOFF", "pv_kw": 4.21, "load": "PRE_COOLER"}
Hard invariant: only the FreeRTOS state machine switches power; a manual IP67 switch overrides.
K
Krishi Mitra
WhatsApp voice advisory · Nashik cluster
रामभाऊ, तुमच्या टोमॅटोच्या मुळांना पुरेसे पाणी मिळाले आहे (४४.८%). पंप सुरक्षितपणे बंद झाला असून सौर वीज शीतगृहाकडे वळवली आहे.
0:14 / 0:26
Translation: “Rambhau, your tomato roots have reached optimal moisture (44.8%). Pumping stopped safely; solar power now runs the cold room.”
धन्यवाद! उद्या पाणी कधी सुरू होईल?
UX artifact: 20-second voice notes at key state changes (pumping done, cold room online); built for zero-literacy use.
AI architecture: deterministic agentic RAG · FastAPI backend · FreeRTOS edge firmware · Pydantic schema. Marathi text to be reviewed by a native speaker before field use.
AgroStruxure™ · 07 / 10
Notes: TRUST (40 s). Farmers do not use dashboards, so the interface is a 20-second WhatsApp voice note in Marathi or Hindi, sent at state changes: pumping done, cold room online. The model is deliberately boxed in: stage 1 the MCU logs telemetry; stage 2 Pydantic validates the JSON and blocks the LLM if data is missing; stage 3 a read-only RAG prompt sees only telemetry and agronomy templates; stage 4 TTS. LLMs never control contactors; all switching is by the deterministic FreeRTOS state machine and a manual override on the IP67 box. This screen is also the UX design artifact requested in the Challenge 01 deliverables. Control works offline; the advisory needs 4G.

## Slide 8
COMMERCIAL FEASIBILITY · UNIT ECONOMICS
₹50,212 Net Capex per Farm, Payback in 2.0 Years
A farm's share of a 4-farm pre-cooler after the 35% subsidy. The ₹7,540 edge controller is separate and pays back in 1.5 years.
Capex waterfall, ₹ thousand per 4-farm cluster
Chart: 
| Gross pre-cooler | Shared PV avoided | Net system | 35% subsidy | Cluster net | Per farm (÷4)
base | 0 | 309 | 0 | 200.85 | 0 | 0
value | 400 | 91 | 309 | 108.15 | 200.85 | 50.2
Cumulative cash flow per farm, ₹ thousand
Chart: 
| Day 0 | Month 6 | Month 12 | Month 18 | Month 24
Cumulative cash flow | -50.212 | -37.546 | -24.88 | -12.214 | 0.452
Annual farmer gain
₹25,332
₹15,732 spoilage + ₹12,000 timing − ₹2,400 opex
Edge controller BoM
₹7,540
Pays back in 1.5 yr; ≈1.9 yr combined with the cooler share
Tier B FPO hub (5 MT)
4.2 yr
Own array, leasing: ₹780k net capex, ₹184k/yr net revenue
Assumes 35% MIDH/AIF support (3.0 yr payback without it), ₹35,000/kWp PV, 30 t/ha yield, ₹12/kg. Excludes drip hardware (assumed in place) and the host farm's PV. Controller benefit (~₹5,000/yr) is not in the ₹25,332. Model: research/08_IMPACT/impact_model.py (1 ha tomato, Nashik, 4.8 kWp PM-KUSUM Component B pump).
AgroStruxure™ · 08 / 10
Notes: ECONOMICS (60 s). Gross 2 MT pre-cooler (compressor + PCM) Rs 400,000. It needs no PV of its own because it runs on the host farm's idle surplus, avoiding 2.6 kWp x Rs 35,000 = Rs 91,000. Net Rs 309,000. 35% MIDH/AIF support = Rs 108,150, leaving Rs 200,850 for the cluster, Rs 50,212 per farm. Annual gain Rs 25,332: payback 1.98 years (3.0 without subsidy). Month-by-month: -50.2k at day 0, -37.5k at month 6, -24.9k at month 12, -12.2k at month 18, +0.5k at month 24. 2.0 years = 4 harvests at 2 cycles per year. Edge controller BoM Rs 7,540 (ESP32-S3, MAX485, FDR probes, SHT31, pyranometer, flow meter, latching valve, 2 TeSys D, SMPS, SIM7600, IP67 enclosure); standalone payback 1.5 years = 3 seasons on ~Rs 5,000/yr of water, pump-health and yield protection. Combined (57,752 / 30,332) = 1.9 years. Tier B 5 MT FPO hub pays back in 4.2 years. Not included: drip hardware, which the saving assumes is already installed.

## Slide 9
DEPLOYMENT · DE-RISKED SCALING
From Digital Twin to a 250-Farm Pilot
Each phase has an exit gate. Targets below are plans, not results.
PHASE 1 · Q4 2026
Digital twin
0 physical units
• 365-day energy, water and thermal model that reconciles to zero discrepancy
• Modbus state machine emulating ATV320 (Reg 8501 / 8502)
• Marathi / Hindi advisory prototype
Exit: mass and energy balances reconcile
PHASE 2 · Q1–Q2 2027
Hardware-in-loop bench
1 testbench
• ESP32-S3 with ATV320 and motor dynamometer
• 500 DC transfer cycles with the 5 s dead-band
• Type-2 DC SPD surge endurance at 1,000 V DC
Exit: 500 faultless transfers, no drive trip
PHASE 3 · Q3–Q4 2027
Nashik FPO pilot
20 farms · 5 clusters
• Real tomato harvests with continuous FDR monitoring
• One shared pre-cooler per 4-farm cluster
• Daily WhatsApp voice notes to farmers
Exit: >35% water saving, ≥95% pre-cooler uptime over 2 seasons
PHASE 4 · 2028
Commercial expansion
250 farms · 5 FPOs
• Factory-assembled DIN-rail retrofit kits
• Urja Mitra: local ITI-trained technicians
• Catalogue option with Schneider rural EPCs (proposed)
Exit: break-even on 5 FPO contracts
Enablers PM-KUSUM Component B (≈10.06 lakh pumps installed, 4.67 lakh in Maharashtra) · Atal Bhujal Yojana · MIDH / AIF 35%. Proposed partners (not yet confirmed): Sahyadri Farmers Producer Co., Nashik; Schneider Electric rural EPC channel.
Installed-pump counts: MNRE PM-KUSUM progress reports (31 Jan 2026; Maharashtra figure 30 Nov 2025), as reported. Phase dates and exit gates are targets.
AgroStruxure™ · 09 / 10
Notes: ROADMAP (40 s). Four gated phases. Phase 1 (now, Q4 2026) is the software digital twin: 365-day energy, water and thermal balances, Modbus emulator, vernacular prototype; this is what Phase 2 of the hackathon (Oct 11 - Nov 22) builds on. Phase 2 hardware-in-loop bench with an Altivar ATV320 and dynamometer: 500 faultless DC transfers. Phase 3 a 20-farm, 5-cluster pilot in Nashik: exit gate is more than 35% measured water saving and 95% pre-cooler uptime over two seasons. Phase 4 250 farms across 5 FPOs. MARKET: about 10.06 lakh Component B pumps installed by 31 Jan 2026 (13.3 lakh sanctioned), 4.67 lakh in Maharashtra (Nov 2025) - confirm on the MNRE dashboard before quoting. Sahyadri FPO and Schneider's rural EPC channel are PROPOSED partners; no agreement exists yet - say so if asked.

## Slide 10
EXECUTIVE SYNTHESIS · YUVA YODHA 2026
One Solar Pump. Four Measured Outcomes.
A connected retrofit layer for Altivar Solar drives and TeSys switchgear that turns standalone pumps into community microgrids.
41.2%
LESS GROUNDWATER
7,000 m³ per ha per year; full crop requirement still met
4,137 kWh
IDLE SOLAR UNLOCKED
per farm per year once water is right-sized; cooling a 4-farm cluster uses 1,062 kWh
1.31 t
TOMATOES SAVED
per ha per year; farm-stage loss 8.37% → 4.00%
2.0 years
CAPITAL PAYBACK
₹50,212 net capex per farm; ₹25,332 net gain per year
Sustainability 0.39 t CO₂e per ha per year (embodied emissions of avoided spoilage) · 7,000 m³ groundwater conserved · no diesel, no battery
Sanskar Tiwari
Embedded firmware and lead
FreeRTOS state machine, Modbus RTU, CiA402 drive control
Shambhavi Patil
Geospatial intelligence
Sentinel-2 NDVI/NDWI, dynamic FAO-56 Kc curves, aquifer balance
Kanishka Salgude
Electrical systems and VFD
Altivar ATV320 configuration, TeSys D interlocking, DC routing
Chaitanya Ranade
Product and agronomy
FPO cluster economics, MIDH/AIF subsidies, vernacular WhatsApp UX
Schneider Electric synergies: Altivar Solar OEM pre-installation · EcoStruxure microgrid edge integration · SE Ventures cleantech scale. Challenge 01: Sustainable Agriculture. Model: research/08_IMPACT/impact_model.py (1 ha tomato, Nashik, 4.8 kWp PM-KUSUM Component B pump).
AgroStruxure™ · 10 / 10
Notes: CLOSE (30 s). Four measured outcomes per hectare: 41.2% less groundwater, 4,137 kWh/yr of idle solar unlocked (of which a 4-farm pre-cooler uses 1,062 kWh), 1.31 t of tomatoes saved, 2.0-year payback. Carbon claim is deliberately modest: 0.39 t CO2e/ha/yr, embodied emissions of avoided spoilage. For Schneider: Altivar Solar drives pre-installed with the controller, EcoStruxure-aligned edge integration, and a cleantech scale path via SE Ventures. Confirm team roster and roles before submission.